## Slide 1: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 1 – Staining from drips inside separator shed. Note: Separators are inside lined containment.
Photo 2 – Staining from drips inside separator shed. Note: Separators are inside lined containment.

## Slide 2: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 3 – Staining from drips inside separator shed. Note: Separators are inside lined containment.
Photo 4 – Lined containment berm around all separators.

## Slide 3: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 5 – Production area inside lined containment.
Photo 6 – Drip catch liners inside lined containment.

## Slide 4: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 7 – Drip catch liners inside lined containment.
Photo 8 – Drip catch liners inside lined containment with staining adjacent to drip catch.

## Slide 5: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 9 – Perimeter stormwater controls, no sheen or staining observed.
Photo 10 – Perimeter stormwater controls, no sheen or staining observed.

## Slide 6: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 11 – Staining beneath scrubber, not inside lined containment.
Photo 12 – Meltwater inside containment around production tanks. Hydrocarbon sheen and paraffin noted.

## Slide 7: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 13 – Meltwater inside containment around production tanks. Hydrocarbon sheen and paraffin noted.
Photo 14 – Workover rig was tripping out pipe at time of inspection.

## Slide 8: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 15 – Water from pipe near workover rig and wellhead. Product observed on water.
Photo 2 – Chemicals inside containment were observed throughout inspection.

## Slide 9: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Operator Provided Photo 1 – Staining at scrubber cleaned up.
Operator Provided Photo 2 – Staining at separator cleaned up

## Slide 10: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Operator Provided Photo 3 – Staining at separator cleaned up
Operator Provided Photo 4 – Staining at separator cleaned up

## Slide 11: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Operator Provided Photo 5 – Staining at separator cleaned up
Operator Provided Photo 6 – Staining at separator cleaned up

## Slide 12: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 1 – Site overview, silt fence damaged by wind, fencing down.
Photo 2 – Excavation. Fencing down.

## Slide 13: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Photo 1 – Site overview, silt fence damaged by wind, fencing down.
Photo 2 – Excavation. Fencing down.

## Slide 14: Inspection Photos Location Name: Cub-Creek Knight Pad Facility ID: 457362
Operator Provided Photo 7 – Staining at separator cleaned up